WORKING GROUP:	Network Working Group

TASK:	TIF 014

FILE NAME:	NTCO0333.doc

TITLE:	Typical Call Flow using SIP for VoIP at the NNI

ISSUES ADDRESSED:	Bell Canada presents some typical basic call flow for calls using SIP at the network to network interface

SOURCE:	Douglas Kwong

(Douglas.kwong@bell.ca)

Bell Canada

DISTRIBUTION:	NTWG members

NOTICE:	This contribution is being submitted by Bell Canada as a basis for discussion.  This should not be construed as a binding proposal on the part of Bell Canada.  Specifically, Bell Canada reserves the right to add to, amend, or withdraw the contents of this contribution.

DATE:	Sept 9, 2005

(A) Introduction

On July 19 meeting, it was proposed that a number of participants are to submit contributions outlining various call flow scenarios regarding the mapping of minimum message set between SS7 and SIP.

This contribution specifies the 3 typical call flow scenarios for each signalling mechanism: basic call control for successful call attempt, basic call control for unsuccessful call attempt – termination busy and call forward on busy.

The material in this contribution is focused on network-to-network interface and no assumption is made as to the technology type of the end-users’ terminals.  For example, user A may be connected to network A via analog facility, ISDN or broadband technology.  Hence the terms such as “off-hook”, “on-hook” and “dialling” are purely for illustrative purposes only.

(B) Typical SS7 Basic Call Control Call Flow

The following 2 figures (Figure 1 and Figure 2) represent basic call control functions and messaging specific for local calling scenarios without continuity check: one for successful call attempts and one for encountering called party busy.

Figure 1: SS7 Successful Call Attempt – Basic Call Control

Figure 2: SS7 Call Attempt – Called Party Busy

(C) Typical SIP Call Control Call Flow

As per Section (B), Figures 3 and 4 depict the basic call control using SIP messaging for a call set up and take down: one for successful call attempts and one for encountering called party busy.

Figure 3: SS7 Successful Call Attempt – Basic Call Control

Figure 4: SS7 Call Attempt – Called Party Busy

(D) Typical Call Forwarding Call Flow

The following diagrams provide the call forward feature scenarios for both SS7 and SIP.

Figure 5: SS7 Call Forwarding on Busy

Figure 6: SIP Call Forwarding on Busy

# Text boxes

(User B in off-hook state)

REL (w cause)

(User B in on-hook state)

Conversation

(User B goes Off-hook)

(User B in on-hook state)

200 OK

Bye

RLC

(Off-hook and Dialling)

IAM

User B

User A

Network B

Network A

ANM

REL (w cause)

(Off-hook)

RLC

ACM

(Off-hook and Dialling)

(On-hook)

(Alerting)

IAM

User B

User A

Network B

Network A

(Disconnect)

Conversation

200 OK

ACK

180 Ringing

100 Trying

(Off-hook and Dialling)

Invite

User B

User A

Network B

Network A

(User B in on-hook state)

200 OK

Ack

486 Busy Here

100 Trying

(Off-hook and Dialling)

Invite

User B

User A

Network B

Network A

REL (w cause)

Conversation

RLC

ANM

Off-hook

ACM

ACM

Alerting

IAM

Network C

(User B in on-hook state)

User C

(User B in off-hook state)

ANM

REL (w cause)

RLC

(Off-hook and Dialling)

(On-hook)

IAM

User B

User A

Network B

Network A

On-hook

100 Trying

100 Trying

200 OK

(Ringing)

180 Ringing

Invite

Conversation

Bye

180 Ringing

Network C

User B in on-hook state

User C

User B in off-hook state

Bye

200 OK

(Off-hook and Dialling)

Invite

User B

User A

Network B

Network A